## Slide 1: Geotechnical data standardization
Viewpoint from Geotechnical FEM package

## Slide 2: Building Information Model
Combines most aspects of project development above ground
Structural analysis packages oversimplify interaction with soil
Common missing component - > Subsurface

## Slide 3: Risks associated with disregarding soil

## Slide 4: Geotechnical finite element analysis
PLAXIS 2D, 3D, MoDeTo
Soilvision, SVFlux, SVSlope etc.
Soil-structure interaction
Advanced models for behavior of soil and rock

## Slide 5: Making a Geotechnical FE model
Create block of soil
Import (or create) structure
Define additional loads
Simulate construction process
Calculate
Assess (development of) forces, settlements etc.

## Slide 6: A Simple block of soil?
Uncertainty / spatial variability
  Continuity of soil layers
  Soil properties
  Reworked samples
  Engineering judgement
More subsurface data can reduce the uncertainty and associated risk
Storing geotechnical data in a centralized, structured and accessible manner could help

## Slide 7: Subsurface model – Survey data
Constitutive models
Survey data
Lab tests
Bore logs
Creation of surface in CAD package
Import into software

## Slide 8: Subsurface model – Bore logs
Constitutive models
Survey data
Lab tests
Bore logs
Determine soil properties
Layers and layer thickness
Create boreholes in software

## Slide 9: Subsurface model – Lab tests
Survey data
Lab tests
Bore logs
Used to derive soil & model parameters
Stiffness Moduli, Creep
Correlations

## Slide 10: Subsurface model – Constitutive models
Constitutive models
Survey data
Lab tests
Bore logs
Describes behavior of (specific) soils
Unloading / reloading
Hardening
Creep
Select model and input in software

## Slide 11: Overview of data input PLAXIS 3D
Notes: Oveiw

## Slide 12: Subsurface information model
Start with factual data:
Survey tools
Logging tools
Lab equipment
Building Information Model
Of importance for information model:
Requires interpreted data
Varying interpretations with same factual data
Insight into assumptions
Use additional labtests, bore logs during project

## Slide 13: Subsurface information model
Site monitoring tools
Earthquake data
New tools assisting in reducing uncertainty & risk?
Model parameter estimation
Inverse analysis tools
Interpreted (3D) geological/soil model
Understanding soil to reduce
risk during and after construction
Adopting to a standard?
Should users tell us what they want?
Interpreted geological / soil model
Digital availability of geotechnical data stored in a centralized, structured and accessible manner, to retain, maintain and update data during project lifecycle