## Slide 1
Standardization and use of ‘geotechnical’ data in Switzerland -
A first approach and problems encountered
Stefan Volken
Geotechnical Data Standardization Workshop Paris, 22 - 24 January 2019

## Slide 2: SGS Tasks
  Managing Geological information between the Earth’s surface and 5’000 meters depth  Dealing with a wide scale range (local to national)
  Geological (incl. hydrogeological and geotechnical) data are required for various uses and hazard management above and below ground.  The challenge of standardizing geological data  Need of data and tools for planning of competing underground uses

## Slide 3
Uses and hazard prevention in the (shallow) subsurface
Hydrogeology
Earthquake prevention
Building / City Information Modeling (BIM / CIM)
Materials management: Mineral raw materials, contaminated sites, landfills
, …
Geothermics
Geotechnics
Notes: unterschiedliche Anforderungen an Lockergesteinsuntergrund
unterschiedliche Daten resp. Klassifikationen zum Lockergesteinsuntergrund werden benötigt
ohne gut strukturierte Lockergesteinsdaten ist eine Koordination zwischen den Nutzungen fast nicht möglich  Nutzungskonflikte
damit geologische oder parametrische 3D-Modelle und daraus abgeleitete Produkte erstellt werden können, braucht es einheitlich erfasste und klassifizierte quartäre Lockergesteinsdaten

## Slide 4: Issues with available data
  The available data is very heterogeneous in structure and format.
  The cantons have the sovereignty over the borehole data, thus each of the 26 cantons can actually specify its own guidelines for how the borehole data has to be delivered.
   Therefore a comparison and a common use of the borehole data is almost impossible.  Need for national geological data models

## Slide 5
Existing Data Models

## Slide 6
Pilot areas (Project GeoQuat)

## Slide 7: Availability of geological, geotechnical, hydrogeological and geophysical data
Borehole data (including geotechnical and hydrogeological test results
Geological / geotechnical maps
Geophysical measurements (e.g. cross sections)
Geological cross sections

## Slide 8: Statistics of the captured borehole data
 Good data availability up to a depth of approx. 40 meters
Pilot area | Boreholes | Drilled meters | Individual layers
Birrfeld | 1'577 | 37'230 | 19'830
Visp | 788 | 17'955 | 11'674
Aaretal | 3'280 | 60'215 | 36'275
Vierwaldstättersee | 741 | 15'423 | 8'120
Genf | 615 | 11'240 | 7'143
St. Gallen | 686 | 7'300 | 2'170
Total | 7'687 | 149'363 | 85'212

## Slide 9
Most of the available drilling data in Switzerland is recorded according to the Swiss Standard (SN 670’005a, SN 670'004-1b)
:
1st phase
2nd phase
3rd phase
A code is assigned to each phase
It must be indicated whether the 1st phase code was determined [a] in the laboratory or [b] in the field at the time of drilling, or whether it is [c] a third party interpretation according to the layer description.
Classification of individual layers (1)
Borehole Data Model
clean
silty
clayey
gravel
with
little (<15%)
abundant (15-30%)
much (31-50%)
sand
and with
boulders
stones
organic additives
peat

## Slide 10
In order to cover the entire grain size spectrum, the list of USCS codes had to be extended to include  extended USCS
Classification of individual layers (2)
Borehole Data Model

## Slide 11
SN 670’010: Typical geotechnical parameter values for each USCS class:
Classification of individual layers (3)
Borehole Data Model

## Slide 12
Sediment properties
Density
Plasticity
Humidity
Cohesion
Classification of individual layers (4)
Borehole Data Model

## Slide 13
Chart: 
| 125 | 125 | 118 | 110 | 110 | 101 | 100 | 100 | 100 | 100 | 100 | 100 | 95 | 86 | 83 | 80 | 78 | 62 | 62 | 55 | 55 | 52 | 50 | 49 | 46 | 45 | 35 | 32 | 31 | 30 | 27 | 20 | 20 | 15 | 15 | 13 | 9 | 8 | 7 | 7 | 5
Bachschuttablagerung_Gamsa | 6.6 | 12.5 | 6.5 | 15.3 | 12.2 | 4.8 | 8.9 | 3.2 | 9 | 12.5 | 8.5 | 14.2 | 3.5 | 15.3 | 10.9 | 3.5 | 15.15 | 7.9 | 3 | 6.5 | 3.6 | 20 | 3.6 | 12 | 14 | 10 | 8.8 | 18 | 13.9 | 16 | 11.6 | 11.7 | 10.3 | 3.6 | 10 | 7.3 | 8 | 12 | 7.2 | 16.4 | 4
Bachschuttablagerung_Saltina | 15.65 | 12.4 | 17.5 | 9.2 | 7.6 | 4.4 | 5.5 | 6.9 | 4.1 | 4.9 | 13.4 | 3.9 | 4 | 10.2 | 10.2 | 7.9 | 12 | 8.6 | 4.6
Bergsturzmaterial | 21.1 | 24 | 17.1 | 25 | 22.1 | 25.2 | 33.6 | 35.8 | 24 | 21.7 | 26.6 | 11.75 | 15.4 | 10 | 10 | 12.8 | 30 | 24.2 | 15.8 | 16.2 | 19 | 19 | 21.5 | 27.3 | 23.8 | 18.7 | 12.2 | 21 | 5.5 | 8 | 13.25 | 17.9 | 12.3 | 24.7 | 20.9 | 12.6 | 24 | 19.3 | 14.9 | 9.6 | 17.6 | 9.2 | 13.6 | 3.6 | 6 | 15.7 | 16.9 | 3 | 3.2 | 6 | 9.8 | 14.6
Fels | 13.05 | 14.3 | 14.5 | 14.25 | 6.4 | 14.15
Gehaengeschutt | 6 | 7.1 | 11.2 | 15 | 9.1 | 8.3
Kuenstliche_Ablagerung | 3.4 | 3.5 | 3.5 | 4.3 | 4 | 2.8
Kuenstliche_Ablagerung_Lonzadeponie | 1.2 | 3.3
Limnische_Ablagerungen | 16.15 | 15.3
Moraenenmaterial | 4
No. of spt hits
Depth of spt start below surface
Limited use of Standard Penetration Tests (SPT)
Borehole Data Model

## Slide 14
Enabling automation through standardization

## Slide 15
Enabling automation through standardization

## Slide 16
Pilot areas
Geneva

## Slide 17
3D Buildings
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 18
3D Buildings
(underground)
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 19
Geothermal probes
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 20
Sheet piles, piles, anchoring zones etc.
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 21
Register of sewage pipes
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 22
Tunnel (virtual)
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 23
Overview of underground construction data
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 24
Boreholes
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 25
Boreholes + geological cross sections
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 26
Boreholes + geological cross sections + geological map
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 27
Geological 3D model (Voxel model)
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 28
Cross sections of geological voxel model
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 29
Rockhead surface
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 30
Hydrogeological data  groundwater table
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 31
Overview of all data (without geological 3D model and groundwater table)
Comparison: underground construction data  underground geological / geotechnical data
BIM / CIM and Geology

## Slide 32
Interaction of construction data and geological data with the help of spatial queries / analyses, e.g. tunnel project planning
BIM / CIM and Geology

## Slide 33
Interaction of construction data and geological data with the help of spatial queries / analyses, e.g. tunnel project planning
BIM / CIM and Geology

## Slide 34
Interaction of construction data and geological data with the help of spatial queries / analyses, e.g. geothermal probes planning
BIM / CIM and Geology

## Slide 35
Post-Products from 3D models

## Slide 36
Ground Foundation Classes Map
Comparison with existing ground foundation class map in Geneva

## Slide 37
Thank you for your attention
stefan.volken@swisstopo.ch