## Slide 1: InfraBIM Guidelines in Finland
Geotechnical Data Standardization Workshop 22.-23.1.2019
Juha Liukas
Leading consultant, InfraBIM Sitowise
Chair of Infra standardizartion group, buildingSMART Finland

## Slide 2: Common InfraBIM Guidelines
InfraBIM Classification System
  ’The language’
  InfraBIM Terminology
InfraBIM Requirements
  YIV Yleiset Inframallivaatimukset
  What and how to model in different phases
  the updating will be published 3/2019
Open Data Exchange
  Inframodel4 (LandXML)
  IFC (bridges, engineering constr.)
  Infra-format for bore hole data
  GML
Notes: There are the main results of InfraFINBIM and the three main pilars of InfraBIM were
InfraBIM-classification system
InfraBIM modelling requirements
Inframodel data tranfer; and as you see for bridges we have used IFC allready earlier
By the data delivery these things have to be in order

## Slide 3
Standardized Structure for Information and Documentation, Standardized Data Transfer
Notes: So once again OpenBIM approach
Standardized structure for information and documentation
Suitable for alla kind project
Software independent

## Slide 4: InfraBIM Classification
Unified numbering and designation practice for infrastructure models throughout life cycle
Numbering system is compatible with building element classification
Main role in construction layers and surfaces and string lines
https://buildingsmart.fi/infrabim/infrabim-nimikkeisto/
Notes: InfraBIM Classification is developed in the Infra FINBIM program in 2012
The goal is to have a unified numbering and designation practice for infrastructure models throughout life cycle
The numbering system of surfaces is compatible to building element classification. So it is based to the building elements, but it do not fullfill all needs of information modelling
In the classification main role is in construction layers and surfaces and the string lines
InfraBIM classification includes 3D and cross section pictures for visualisation

## Slide 5: InfraBIM Classification – subsoil model
Surface types
Interprection codings
Soil surfaces
Rock surface
Target surfaces

## Slide 6
Inframodel3 > Inframodel4
Structural surfaces: fences and railings
Lower surface of the structure
Line models of structures
Lower surface of clay
Upper surface of the structure
Complete model
Ground, lower surface of the clay
Upper surface line model
Drying, bases
As-built data
Sub soil model
Surface structures
Structural layers
New network types
Bases
Wire and cable routing
Railings and fences
Column stabilisation
20.1.2019
Notes: And Inframodel, I have to mention that
Now we’ll take the next step Inframod4, it includes new parts ans properties, e.g. materils, networks, …
Inframodel development has also served as a very good foundation to understand and act to the international standardization.
With that we have influenced also to IFC ’Infra’ development

## Slide 7: Common InfraBIM Requirements 2018
Yleiset tietomallivaatimukset ja -ohjeistukset
1. Common
2. Intial State
3. Plan & Design
4. Construction
5. Maintanance
https://buildingsmart.fi/yleiset-inframallivaatimukset-ohjeiden-paivitys-lausuntopyynto-yiv-2018/
20.1.2019
InfraBIM Guidelines Juha Liukas

## Slide 8: Intial State model

## Slide 9: Inframodel4 – Subsoil model – soil properties
GEO-soiltype: Tv, Sa, Si, Hk, SrMr, siMr, …
Quality for construction: S1-S4, H1-H4, U1-U4
Frost cofficient
E-modul
<Feature code="IM_coding" source="inframodel">
<Property label="surfaceCoding” value=”31” />
<Property label="surfaceCodingDesc” value="Maalajirajapinta” />
<Property label="soilTypeGEO" value="Si" />
<Property label="soilTypeISO" value="Ci" />
<Property label=”qualificationClass" value=”U3" />
<Property label=”frostSwellingFactorWet" value=”6" />
<Property label=”elasticModulusWet" value=”10" />
</Feature>
N. Yabukin Representation of caves in a shield tunnel product model
TIN surfaces between layers (interprediction points and lines)
20.1.2019 Juha Liukas
InfraBIM Guidelines

## Slide 10: Borehole data Infra-format National standard
TT PA 1 -
XY 74767.910 34397.400 11.680 20051991 760
.000 .00 0
.200 .00 0 Hm
1.500 50.00 0 Sa
5.000 25.00 0
5.200 100.00 8 Si
5.600 100.00 0 Sa
5.800 100.00 100 Hk
5.900 100.00 100 Ki
6.400 .00 -5
6.600 100.00 16
6.800 100.00 53
7.000 100.00 80
7.100 100.00 100
8.000 .00 -5
8.100 100.00 100
8.700 .00 -5
-1 KI
TT NE 1 -
XY 74767.910 34397.400 11.680 20051991 760
.500 - .500 SA
LB w 37.800 %
1.000 - 1.000 SA
LB w 46.200 %
2.000 - 2.000 SA
LB w 82.300 %
LB F 57.600 %
LB VG 15.300 kN/m3
3.000 - 3.000 SA
LB w 61.700 %
LB F 57.600 %
LB VG 16.500 kN/m3
4.000 - 4.000 SA
LB w 82.900 %
LB F 43.800 %
LB VG 15.100 kN/m3
5.000 - 5.000 SA
LB w 47.600 %
LB VG 17.100 kN/m3
-1
TT SI 1 -
XY 74767.910 34397.480 11.650 11091991 760KL
1.000 40.00 5.80 .00
1.500 17.00 1.60 .00
2.000 12.70 1.90 .00
2.500 11.10 1.60 .00
3.000 9.50 2.40 .00
3.500 12.20 2.10 .00
4.000 13.50 2.70 .00
4.500 10.60 3.20 .00
5.000 12.20 3.70 .00
20.1.2019 Juha Liukas
InfraBIM Guidelines

## Slide 11: Subsoil model – utilising
Target surfaces
Road/rail construction – subsoil integration
Bridge / engineering structures - subsoil
QTO quantity take off
Geotechnical calculation
Machine quidance

## Slide 12: Future Challenges
Geotechnical part is missing from COBIM
Consolidation of BIM- and InfraBIM -requirements
Consolidation of Talo- and Infra-classifications
The right standards ? IFC, GML, …
https://rastiprojekti.com/

## Slide 13: Thank you ! Questions ?
juha.liukas(at)sitowise.com