## Slide 1: Underground Environment Representation in MUDDI
Josh Lieberman & Scott Simmons
23 January 2018

## Slide 2: Underground Infrastructure Information (UGII) – Current State of Affairs –
Present UGII data quality is poor
  Different data models
  Stored in different ways
  Different geometry and semantics
Inability to exchange UGI data
  Maintainers have different purposes
  Ownership, governance challenges
  Interoperability issues
Costs of UGII failures are recognized
  Routine excavations can be disastrous
  Inefficiencies in construction
  Unable to predict cascading failures
OGC Underground Concept Development Study Report
http://docs.opengeospatial.org/per/17-048.html

## Slide 3: Use cases and perspectives
Data Use Cases
  Routine street excavations
  Emergency response
  Utility maintenance programs
  Large scale construction projects
  Disaster planning and response
  Smart cities programs.
Data Perspectives
  Data integration
  Visualization – 2D, 3D, 4D, AR
  Data quality, consistency, alignment
  Dependency analysis
  Digital twinning and simulation / predictive modeling
Notes: Many reasons why underground data is critical.
Each use case requires a particular perspective or set of perspectives
Each perspective requires the appropriate geometric constructs, feature attributes, and interrelationships
Some use cases (e.g. excavation) require relatively simple and simply represented data, although it needs to be complete and accurate in 2D.
Some of the most compelling use cases (e.g. emergency response, disaster planning) require relatively complex and accurate data, such as functional dependencies

## Slide 4
Notes: Deodatis – Columbia: too often the underground infrastructure is conceptualized as hanging space, just temporarily hidden by ground, pavement, etc.

## Slide 5: “Nobody Knows What Lies Beneath New York City” Greg Milner Bloomberg Businessweek, 8.10.17
https://www.bloomberg.com/news/features/2017-08-10/nobody-knows-what-lies-beneath-new-york-city
Notes: The underground environment is not just structures hanging in space.
It is a complete whole that resists gravity, upholds ground-level and above-ground city structures, contains below-ground structures such as subways, and provides the pathways for water, air, and other materials to move and transform.
Nobody knows what (and where) is built beneath a (New York) city, nor what it is built in. At least infrastructure has typically a standard form such as a pipe, but the forms of geology, hydrology, pedology in the underground environment are endlessly variable according to natural and artificial influences.

## Slide 6
Underground structures, properties and hazards affect where, and how, to build most effectively
  The Institution of Civil Engineers estimate that about 50% of cost and time over-runs on civil engineering projects are caused by 'unforeseen ground conditions.‘
Dense urban environments = conflicting demands on the subsurface
  Holistic approach needed to avoid developments being considered in isolation
Infrastructure is affected by, and affects, dynamic, complex, underground mass and fluid processes
  Groundwater
  Contamination
  Heat
  Shrink / swell
  Sink holes
  Weathering and corrosion
Geological properties & processes matter
Notes: MUDDI (Model for Underground Data Definition and Integration) focuses for now on representing the underground environment in relation to infrastructure, but those relationships can still be very complex, depending on original geologic processes, long periods of construction, demolition, and reconstruction, as well as the dynamic effects of groundwater, surface processes, chemical and biological transformations, e.g. rotting pilings, subsidence, erosion, development of leakage pathways

## Slide 7
Soil Heterogeneity in 2D.
Notes: Just looking at soil in 2D shows the potential complexity. Equal complexity extends in the 3rd dimension. Most of the above geometric shapes and associated boundaries are interpreted from lithological variation and may or may not correspond to variation in engineering properties, hydrology zones, or chemical characteristics.

## Slide 8: Reference underground environment models
BGS National Geological Model
GeoSciML
EarthResourceML
INSPIRE Geology
GeoTOP
GroundwaterML
SoilIEML
Models are designed for different purposes (engineering, water management, hazard assessment). The model intents need to be understood to allow for meaningful translation and combination between them.

## Slide 9: Underground environment for engineering
A variety of study perspectives (may be overlapping):
  Geology – study of deposited / intruded / precipitated earth materials and their structures, particularly how they got that way.
    Pedology – just the soils created by insitu weathering and bio-transformation
    Hydrology – underground environment as a segment of the water cycle
  Geo(logical) engineering – leveraging geologic knowledge for engineering purposes
  Engineering geology – deriving engineering properties from geologic knowledge
  Geotechnical engineering – determining engineering properties of earth materials with respect to design requirements
A variety of spatial geometric perspectives (may co-exist / overlap)
  “Continuous field” – voxel perspective (complete but not insightful)
  Visual – surface mapping / boring / interpretive cross-section perspectives
  Unit – geologically interpreted units, contacts, structures
  Earthwork – regions determined by engineering role and/or ownership
  Bedding – immediate environmental contexts such as fill volumes around a sewer pipe
Notes: A wide (wild) variety of model perspectives are required to properly represent knowledge of the urban underground.

## Slide 10: Drawing from GeoSciML / Inspire

## Slide 11: Drawing from LandInfra

## Slide 12: Drawing from IFC
Geotechnical Extension

## Slide 13: MUDDI integration opportunities
Notes: Targeted at levels of commonality and detail that would be relevant to underground infrastructure data integration.

## Slide 14: Model Patterns
Node
Specialization Adaptation Relation
Attribute 1
Attribute 1
Attribute 2
Attribute 1
Attribute 2
Attribute 3
Attribute A
Method X
Attribute A
Method X
Network Element
Link
Network
ConnectTo
Partof
Structure
Network
Structure
Electrical
Component
Notes: Three ways of representing connections between features:
Specialization – from general to specific, but carries along all attributes
Adaptation (MUDDI interfaces, GeoSciML abstract blocks) adds attributes and operations where needed without as much baggage
Relation: topological or functional relationships between features, such as in a network, or composite

## Slide 15: MUDDI Model Structure
Core Structures
2D Geom
Core Model Elements
Network Structures
Environment Regions
Containers & Supports
Input / Output / Detail Interfaces
3D Geom
Surveys
Sensors
CityGML
BIM - IFC
Assets
Section
Borehole
Engineering Parameters
Data Quality
Network
Graph
Specialized
Structures
Supply Regions
Control Function
Inputs
Outputs
Notes: Everything is a structure
Some structures are networks / part of networks
Some structures are defined regions of underground geology / hydrology / chemistry
Some structures mainly contain or support other structures
Interfaces support specific attributes of structures and/or enable specific types of operations
Spatial:
  Core structures have identity and location for asset management
  2D interface adds 2D extent (plus elevation) for excavation design
  3D interface adds 3D geometric entities for construction design, modeling, etc.
  CityGML interface provides access to data as CityGML for modeling and visualization
  BIM-IFC interface provides access to data as Industry Foundation Classes for engineering and O&M
Engineering parameters could represent geotechnical properties as well, but this is not presently shown
Utility networks
  Structures are networks, links, or nodes
  One network can be part of or subordinate to another network
  Nodes can have internal networks
  Links can connect nodes of the same or different networks (interlinks)
  Network graph interface adds connections between network structures
  Supply regions interface adds 2D / 3D supply region geometries with inputs and outputs (e.g. a substation circuit )
  Control function interface adds operational functions and status

## Slide 16: Core MUDDI Model
Notes: MUDDI allows for defining any needed environment object, with arbitrary 2D / 3D geometry and optional borehole / x-section interfaces, then subdivided into material types which may partially overlap with each other in space (e.g. curved geo-object, inclined water table, horizontal soil unit, roll-front redox zone). Geotechnical properties are not currently represented in a conceptual interface but could be added for mapping to specifically geotechnical data models.

## Slide 17: Implementation Strategies
Encodings
  CityGML
  Simple Features SQL
  FME interchange format
  JSON-LD
Datastores
  Separate tables for object subtypes, interfaces
  Unique column entries for each object tuple
  Key-value graphs
Pathways
  Start with core structure data, add interfaces and specializations as applications require
  Start with full complexity, create simplified views where data exists
Designs
  Federation of data providers and consumers
  Virtual federations on common IT infrastructure
  Centralized repositories of authoritative underground data